## Slide 1: Title Page
HAZARD COMMUNICATION STANDARD 2012 (HCS/GHS)
BY
WAYNE STATE UNIVERSITY
FOR
SUSAN HARWOOD TRAINING GRANT
2014-2015

## Slide 2: Refresher Module
REFRESHER MODULE HAZARD COMMUNICATION STANDARD WITH GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION AND LABELING OF CHEMICALS (HCS/GHS)

## Slide 3: ACKNOWLEDGEMENT
UNITED STATES DEPARTMENT OF LABOR Occupational Health and Safety Administration (OSHA) Susan Harwood Training Follow-On Grant
SH-27686-SH5
This material was produced under a grant (SH-26321-SH4) from the Occupational Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does the mention of trade names, commercial products, or organization imply endorsement by the U.S. Government.
Notes: This material was produced under Susan Harwood grant number SH-26321-SH4 Occupational Safety and Health Administration, U.S. Department of Labor, and used for training purposes under the Susan Harwood Training Follow-On Grant SH-27686-SH5

## Slide 4: WORKER RIGHTS UNDER OSH ACT
Workers are entitled to safe and healthful conditions. The OSH ACT provides workers with the right to:
    Ask OSHA to inspect their workplace;
    Review employers’ records of work-related injuries and illnesses
    Get copies of their medical records; and
    Receive information and training about hazards and their prevention, using applicable OSHA standards.
WORKER RIGHTS
UNDER OSH ACT
Notes: Workers are entitled to working conditions that do not pose a risk of serious harm to them. To help ensure a safe and healthful workplace, the OSH Act provides workers with the right to ask OSHA to inspect their workplace; use their rights under the law without retaliation and discrimination; receive information and training about hazards, and the methods for prevention. Under the OSH Act, workers also have the right to ask for the OSHA standards that apply to their workplace, get copies of test results regarding the hazards in the workplace, review records of work-related injuries and illnesses, and get copies of their medical records.

## Slide 5: RIGHTS AS A WHISTLEBLOWER
Workers may file a complaint with OSHA if the employer retaliates by taking unfavorable personnel action against them for whistleblowing.
  for more information Whistleblowers’ Rights
Whistleblower laws require that complaints be filed with OSHA within certain time limits following the alleged retaliation.
RIGHTS AS A WHISTLEBLOWER
Notes: Workers may file a complaint with OSHA if the employer retaliates by taking unfavorable personnel action because workers engaged in protected activity relating to workplace safety or health, asbestos in schools, cargo containers, airline, commercial motor carrier, consumer product, environmental, financial reform, food safety, health insurance reform, nuclear, pipeline, public transportation agency, railroad, maritime, motor vehicle safety, and securities laws. If it is believed that the employer retaliated against the worker because of exercising legal rights as an employee, workers must contact OSHA as soon as possible; the complaints must be filed within the legal time limits. An employee can file a complaint with OSHA by visiting or calling the local OSHA office or sending a written complaint to the closest OSHA regional or area office. Written complaints may be filed by facsimile, electronic communication, hand delivery during business hours, U.S. mail (confirmation services recommended), or other third-party commercial carrier.

## Slide 6: RIGHT-TO-KNOW
Federal Hazard Communication Standard, Title 29, Part 1910.1200 of the Code of Federal Regulations (29 CFR 1910.1200) mandates that “Workers have the right to know and understand the hazardous chemicals they use and how to work with them safely.”
  This regulation is designed to make information about hazardous chemicals that are present in work places available to exposed employees.
  The hazard communication standard applies to any business, including manufacturers that use hazardous chemicals, regardless of the number of individuals employed.
RIGHT-TO-KNOW
Notes: Federal Hazard Communication Standard, Title 29, Part 1910.1200 of the Code of Federal Regulations (29 CFR 1910.1200) mandates that “Workers have the right to know and understand the hazardous chemicals they use and how to work with them safely.” This regulation is designed to make information about hazardous chemicals that are present in work places available to exposed employees. The hazard communication standard applies to any business, including manufacturers that use hazardous chemicals, regardless of the number of individuals employed.

## Slide 7: Purpose
Hazard Communication Standard (HCS)
  OSHA 29 CFR 1910.1200
    classifies chemicals by their hazards
    provides information to employees
PURPOSE
Notes: The purpose of Hazard Communication Standard (HCS - OSHA 29 CFR 1910.1200) is to classify chemicals with respect to their hazards and provide information to employees so they can protect themselves against possible physical and health hazards in the workplace. Under HCS, employees have the right to know necessary information about the chemicals that they are working with, through labels or other forms or warning, safety data sheets, and training.

## Slide 8: HAZARD CLASSIFICATION
    Such as
    Flammable gases
    Explosives
    Gases under pressure
HAZARDS
Physical Hazards
Health Hazards
Environmental Hazards
Such as
Skin corrosion/irritation
Carcinogenicity
Acute toxicity
Acute aquatic toxicity
Chronic aquatic toxicity
Notes: Under HCS, importers and manufacturers are required to classify the chemicals with respect to their hazards by using a full range of available scientific literature or other evidences concerning potential hazards. Hazards are classified under three headings in HCS: Physical Hazards, Health Hazards; and Environmental Hazards. Physical hazards are those which threaten employees’ physical safety, such as flammable gases, explosives, and gases under pressure . Health Hazards are associated with chemicals which pose hazardous effects, such as skin corrosion/irritation, carcinogenicity and acute toxicity. Environmental Hazards may pose a risk of damage to the aquatic environment which are acute aquatic toxicity and chronic aquatic toxicity. OSHA does not mandate the use of environmental hazards in HCS/GHS.

## Slide 9: HAZARD CLASSIFICATION
Degree of hazards
  Harmful effect decreases when category number increases
Category 1
Category 2
Category 3
Category 4
MOST HARMFUL
LEAST HARMFUL
Notes: HCS further classifies Physical, Health and Environmental hazards based on their severity, which is expressed by numbers and letters (as needed). As the category number of the hazard classes increases, the hazard becomes less harmful.

## Slide 10: HAZARD CLASSIFICATION
Specific criteria on chemicals to be classified as hazardous can be found in
  APPENDIX A TO §1910.1200– HEALTH HAZARD CRITERIA, and
  APPENDIX B TO §1910.1200 - PHYSICAL HAZARD CRITERIA
Notes: Detailed information about hazard classifications and categories for physical and health hazards can be found in Appendices A and B of the Hazard Communication Standard. The OSHA website has the links for these appendices.
https://www.osha.gov/dsg/hazcom/hazcom-appendix-a.html (Appendix A)
https://www.osha.gov/dsg/hazcom/hazcom-appendix-b.html (Appendix B)

## Slide 11: GHS LABELS
Labels are
  written, printed or graphic information elements
  attached to the immediate container or package of a hazardous chemical
Notes: HCS defines labels as written, printed or graphic information elements concerning a hazardous chemical that are affixed to, printed on, or attached to the immediate container or package of a hazardous chemical.

## Slide 12: GHS LABELS
Labels must be
  legible, and clearly displayed
  in English. (Other languages can be added if needed)
Labels must be revised within 6 months when new information becomes available
Notes: GHS labels must be legible and clearly displayed. They must be in English, although it is possible to use other languages if needed. Chemical manufacturers, distributors or importers, who become aware of new information about a chemical product, must revise the label within 6 months.

## Slide 13: GHS LABELS
Per HCS, labels must have
  Product identifier
  Symbols (Hazard pictograms)
  Signal word
  Hazard statement(s)
  Precautionary statement(s)
  Name, address, phone number of manufacturer, importer or responsible party.
Notes: Labels must follow a specific format under GHS. It is required that a label include a product identifier which shows how the hazardous chemical is identified, such as chemical name, code number or batch number; pictograms; signal words; precautionary statements; and name, address, phone number of manufacturer, importer or responsible party.

## Slide 14: PICTOGRAMS
  HCS/GHS has 9 pictograms (environmental is not mandatory)
HCS/GHS
Health Hazard
Flame over a Circle
Skull and Crossbones
Environment
Flame
Exclamation Mark
Gas Cylinder
Corrosion
Exploding Bomb
Notes: Pictograms are standardized symbols that alert workers to the various hazards. Each pictogram consists of a symbol on a white background framed within a red border and represents a distinct hazard(s). There are 9 pictograms used in the new labeling system to convey the health, physical and environmental hazards. OSHA does not mandate the use of environment pictogram. Each pictogram shows the health and safety hazards related to the chemical itself. There can be one or more pictograms on a given label. These pictograms can also be found in Safety Data Sheets containing more information about the chemical product.

## Slide 15: Health Hazard
Carcinogen
Mutagen
Reproductive Toxicity
Respiratory Sensitizer
Target Organ Toxicity
Aspiration Toxicity
Health Hazard
Notes: The first pictogram is a symbol of Health Hazard associated with chemicals that can cause health problems over a long period of time. These are carcinogens which can lead to cancer; mutagens which can cause alterations in DNA; reproductive toxicity which affects the ability of men and women to have healthy children; respiratory sensitizers which can cause allergic reactions after exposure; target organ toxicity hazards which can damage or affect the function of a certain organ; and aspiration toxicity hazards which could lead to chemical pneumonia, and varying degrees of pulmonary problems.

## Slide 16: Flame
  Flammables
  Pyrophorics
  Self-Heating
  Emits Flammable Gas
  Self-Reactives
  Organic Peroxides
Flame
Notes: This pictogram is a symbol of a flame. It is associated with flammable liquids, solids and aerosols. Also indicated by this pictogram are pyrophorics which are capable of igniting spontaneously in air; self heating chemicals which generate heat by reaction with air without any energy supply. It will also appear on chemical products that emits flammable gases, self reactive products** (Type B, C, D, E, F) which are thermally unstable liquid or solid substances or mixtures liable to undergo a strongly exothermic decomposition even without participation of oxygen; and organic peroxides*** (types B, C, D, E, F) which are found in many products such as accelerators, activators, cross-linking agents and curing agents.
**Self reactive types;
Type B- as packaged, does not detonate or deflagrate rapidly but is capable of undergoing a thermal explosion. (Heating causes fire)
Type C – as packaged, possesses explosive properties but will not detonate, deflagrate or thermally explode;
Types D, E, F – have shown hazards such as partial detonation, etc. when tested in a laboratory but do not possess these hazards as packaged.
***Organic peroxide types:
Type B- Any organic peroxide possessing explosive properties and which, as packaged, neither detonates nor deflagrates rapidly, but is liable to undergo a thermal explosion in that package
Type C- Any organic peroxide possessing explosive properties when the chemical as packaged cannot detonate or deflagrate rapidly or undergo a thermal explosion
Type D-
(i)Detonates partially, does not deflagrate rapidly and shows no violent effect when heated under confinement; or
(ii) Does not detonate at all, deflagrates slowly and shows no violent effect when heated under confinement; or
(iii) Does not detonate or deflagrate at all and shows a medium effect when heated under confinement;
Type E-Any organic peroxide which, in laboratory testing, neither detonates nor deflagrates at all and shows low or no effect when heated under confinement
Type F- Any organic peroxide which, in laboratory testing, neither detonates in the cavitated state nor deflagrates at all and shows only a low or no effect when heated under confinement as well as low or no explosive power

## Slide 17: Exclamation Mark
  Irritant (skin and eye)
  Skin Sensitizer
  Acute Toxicity (harmful)
  Narcotic Effects
  Respiratory Tract Irritant
  Hazardous to Ozone Layer (Non Mandatory)
Exclamation Mark
Notes: Exclamation mark pictogram is used on a labels for substances which are: Irritant to skin and eye; skin sensitizer which can cause allergic response following skin contact; acute toxicity which may harm the organs and cause organ damage; chemicals that have narcotic effects, respiratory tract irritant when they are inhaled; and chemicals that are Hazardous to the Ozone layer. OSHA does not mandate to use this pictogram for ozone damage, because it does not directly affect the health of workers.

## Slide 18: Gas cylinder
Gases under Pressure
  Substance is compressed, liquefied, or dissolved at 29 psi or more
Gas Cylinder
Notes: The gas cylinder pictogram will appear on labels of cylinder of compressed gases under pressure. This pictogram on a chemical label means that the substance is a compressed, liquefied, or dissolved gas at 29 pounds per square inches or more.

## Slide 19: corrosion
Skin Corrosion/ burns
Eye Damage
Corrosive to Metals
Corrosion
Notes: The corrosion pictogram appears on containers of chemicals which cause skin corrosion or burns, and eye damage. It is also used for materials which are corrosive to metals.

## Slide 20: Exploding bomb
Explosives
Self-Reactives
Organic Peroxides
Exploding Bomb
Notes: The exploding bomb pictogram is used for explosives which are capable (by chemical reaction) of producing gas at such a temperature and pressure, and at such a speed as to cause damage to the surroundings; self reactives (types A, B)** which are tthermally unstable liquid or solid substances or mixtures liable to undergo a strongly exothermic decomposition even without the participation of oxygen; and organic peroxides (types A, B)*** which are found in many products such as accelerators, activators, cross-linking agents and curing agents.
**Self reactive substance types:
Type A – as packaged, will detonate or deflagrate rapidly;
Type B – as packaged, does not detonate or deflagrate rapidly but is capable of undergoing a thermal explosion. (Heating causes explosion)
***Organic peroxide types:
Type A -Any organic peroxide which, as packaged, can detonate or deflagrate rapidly
Type B - Any organic peroxide possessing explosive properties and which, as packaged, neither detonates nor deflagrates rapidly, but is liable to undergo a thermal explosion in that package

## Slide 21: Flame over a circle
Oxidizers
  substances that release oxygen to another material for purpose of combustion
Flame over a Circle
Notes: This pictogram of a flame over circle associated with materials that are classified as oxidizers. Oxidizers are substances that release oxygen to the another material for the purpose of combustion. They help the materials burn much more rapidly than they normally would. Therefore, they should not be stored close to flammable materials.

## Slide 22: Skull and Crossbones
Acute Toxicity (severe)
  overexposure may be toxic or fatal
Skull and Crossbones
Notes: The skull and cross bones pictogram is used to identify the chemicals which cause acute toxicity hazards. Depending on the toxicity of the chemical, this pictogram indicates that the overexposure of this chemical may be toxic or fatal.

## Slide 23: Environment
Aquatic Toxicity
  toxic to plants and aquatic life
Environment (Non Mandatory)
Notes: The last pictogram, which is environment, appears on chemicals that are considered as toxic to plants and aquatic life. OSHA does not enforce the use this pictogram because it does not directly affect the health of exposed workers.

## Slide 24: SIGNAL WORDS
  Show the severity of possible hazard and lead people to taking precautions.
Signal Words
Warning
Danger
Notes: Signal words emphasize hazards and indicate the relative level of severity of the hazard as assigned to a GHS hazard class and category. Signal words are used to indicate the severity of the possible hazard and lead people to taking precautions. “Warning” and “Danger” are the two signal words used in HCS/GHS.

## Slide 25: SIGNAL WORDS
Warning : used for less severe hazards
Danger : used for more severe hazards
Notes: “Warning” is used for less severe hazards, while “danger” is used for more severe hazards. Since the signal words are assigned according to hazard categories, there can be more than one signal word for each hazard class. However, there will only be one signal word on the label no matter how many hazards a chemical may have. If one of the hazards warrants “Danger” as the signal word and another warrants the signal word “Warning,” then only “Danger” should appear on the label.

## Slide 26: HAZARD STATEMENT
Describes nature of hazard(s) of a chemical for each hazard class (i.e., physical, health, environmental)
Examples
    “Causes serious eye damage through prolonged or repeated exposure.”
    “Toxic if inhaled.”
Notes: Hazard statements are standardized and are assigned phrases that describe the hazard(s) of a chemical for each category of hazard class . Examples are “Causes serious eye damage through prolonged or repeated exposure” and “Toxic if inhaled”.

## Slide 27: PRECAUTIONARY STATEMENT
Measures to prevent or minimize adverse effects of chemicals during handling, transportation or storage.
Examples
    “Keep away from heat, sparks and open flames and store in a cool, well-ventilated place.”
    “Do not eat, drink or smoke when using this product.”
Notes: Precautionary statements are recommended measures to be taken to prevent or minimize adverse effects of hazardous chemical products during handling, transportation or storage. Examples are “keep away from heat, sparks and open flames and store in a cool, well-ventilated place”, or “do not eat, drink or smoke when using this product”. (First aid is included in the precautionary information.) The GHS label should include all appropriate precautionary information. There are four types of precautionary statement: prevention which is used to minimize exposure; response is used to explain what to do in case of exposure; storage shows the requirements for storage and disposal; disposal shows how to dispose the chemical according to regulations.

## Slide 28: SAFETY DATA SHEET
Document containing details of specific hazardous chemicals and their usage.
HCS requires chemical manufacturers, distributors, or importers to provide SDSs to communicate hazards of chemical products
Notes:   Safety Data Sheets (SDSs) are the complete resource for details regarding hazardous chemicals and how the product can be safely used. The HCS requires chemical manufacturers, distributors, or importers to provide SDS to communicate the hazards of hazardous chemical products.

## Slide 29: SAFETY DATA SHEET
16 sections under HCS/GHS (12 mandatory);
    Identification
    Hazard(s) identification
    Composition/information on ingredients
    First-Aid measures
    Fire-fighting measures
    Accidental release measures
    Handling and storage
Notes: The SDS should contain 16 headings, and 12 of these headings are mandatory. First, there should be information about identification of the substance or mixture and of the supplier, with emergency phone number, etc. Second, is the hazard(s) identification section which identifies the hazards of the chemical and the appropriate warning information associated with those hazards such as the hazard classification of the chemical (e.g., flammable liquid, category), signal word, hazard statement, pictogram and precautionary statement. The third section which is Composition/information on ingredients identifies the ingredient(s) contained in the product, including impurities and stabilizing additives such as chemical name, common name and synonym. In the following sections, the first aid measures section describes the initial care that should be given by untrained responders to an individual who has been exposed to the chemical. Fire fighting measures section gives recommendations about suitable extinguishing equipment and special protective equipment or precautions for firefighters, advice on specific hazards that develop from the chemical during the fire. Accidental release measures provides recommendations on the appropriate response to spills, leaks, or releases, including containment and cleanup practices to prevent or minimize exposure to people, properties, or the environment. Handling and storage section provides guidance on the safe handling practices and conditions for safe storage of chemicals.

## Slide 30: SAFETY DATA SHEET
    Exposure controls/personal protection
    Physical and chemical properties
    Stability and reactivity
    Toxicological information
    Ecological information
    Disposal considerations
    Transport information
    Regulatory information
    Other information
Non mandatory
Notes: Exposure controls/personal protection section is about exposure limits recommended by OSHA, Permissible Exposure Limits (PELs), American Conference of Governmental Industrial Hygienists (ACGIH) Threshold Limit Values (TLVs) and manufacturers, engineering controls, and personal protective measures that can be used to minimize worker exposure.
Physical and chemical properties section identifies physical and chemical properties associated with the substance or mixture such as appearance, odor, vapor pressure, pH, relative density, etc. Stability and reactivity section describes the reactivity hazards of the chemical and the chemical stability information such as description of the specific test data for the chemical, any stabilizers that may be needed to maintain chemical stability, etc. Toxicological information identifies toxicological and health effects information or indicates that such data are not available, such as information on the likely routes of exposure (inhalation, ingestion, skin and eye contact, description of the delayed, immediate, or chronic effects from short- and long-term exposure, etc).
Ecological information, disposal considerations, transport information and regulatory information sections are non-mandatory and thus not enforced by OSHA. Ecological information section gives an idea about the ecological impact of the chemical if it is released to the environment, such as the potential for a substance to move from the soil to the groundwater, ozone layer depletion potential etc. Disposal considerations section provides guidance on proper disposal practices, recycling or reclamation of the chemical(s) or its container, etc. Transport information section includes information about classification for shipping and transporting of hazardous chemical(s) by road, air, rail, or sea, such as UN number (four-figure identification number of the substance), UN proper shipping name, etc. Regulatory information section identifies the safety, health, and environmental regulations specific for the product that is not indicated anywhere else on the SDS, such as any national and/or regional regulatory information of the chemical or mixtures (including any OSHA, Department of Transportation, Environmental Protection Agency, or Consumer Product Safety Commission regulations). Other information section is another mandatory section and it indicates when the SDS was prepared or when the last known revision was made. The SDS may also state where the changes have been made to the previous version. You may wish to contact the supplier for an explanation of the changes. Other useful information also may be included in this section.

## Slide 31: SAFETY DATA SHEET
Safety Data Sheet must be in English (Other languages can be added if needed)
Every worker should study the SDS before working with chemicals
If worker needs additional information or have questions, they should ask their employers or supervisors.
Notes: Safety Data sheet must be in English. Although it may be in other languages, if needed. Employers must ensure that the SDSs are readily accessible to employees for all hazardous chemicals in their workplace and every worker should study the SDS before working with chemicals. If worker needs an additional information or have questions, they should ask their employers or supervisors.

## Slide 32: SUMMARY
It is your right to know and understand the hazardous chemicals you use and how to work with them
HCS classifies chemicals by their hazards and provides information to employees
Resources used for information about hazardous chemicals are
  Labels
  SDSs
Notes: It is your right to know and understand the hazardous chemicals you use and how to work with them. HCS classifies chemicals by their hazards and provides information to employees. Resources used for information about hazardous chemicals are labels and SDSs.

## Slide 33: The end
THANK YOU!